## Slide 1: DSM2-PTM and Historical Run
DSM2 Training
September 21,22, and 24, 2009
Kijin Nam
Delta Modeling Section
California Department of Water Resources

## Slide 2: Why Particle Tracking?
Tracking discrete matter in fluid
    Possibility of adding behaviors
  Substitute of contaminant modeling
    Intuitive and simple (faster)
    Not suffers from numerical oscillation problems

## Slide 3: Theory behind DSM2-PTM
Purely kinematic particles with dispersion
  Drifting along flow with dispersion
  No force, no mass
    No buoyancy, etc
  No behavior
Forward Euler Integration
Quasi 3D velocity profile

## Slide 4: Quasi-3D Velocity Profile
Von Karman Logarithmic
Quadratic polynomial
Hydrodynamic Information from DSM2-Hydro
Quasi Velocity profile inside of DSM2-PTM

## Slide 5: Dispersion
Random movement
Vertical View
Transverse View
0
-
s
s
1
-
1
2
E
V
D
t
2
E
T
D
t
0
-
s
s
1
-
1

## Slide 6: PTM in DSM2
Hydro
Flows/Stage
PTM
Particle Information
Hydrodynamic
Information
Particle
Results

## Slide 7: Output Items
Particles in a region
  Form a group of waterbodies using regular expressions
Particle flux
  From a group of waterbodies to another
  Accumulative or instantaneous
  Numbers or percentage
Animation
1
2
3
4
5
6

## Slide 8: Output Formats
DSS format
  Simple
  Item by item
Text format
  Used for animation
Animation binary file

## Slide 9: New in Version 8
Time centered flow
Grid information from a tide file
Slight changes in the input file
Minor bugs are fixed.

## Slide 10: Gotchas
Release particles at least a few days later after the start time of hydrodynamics.
Do not use a group name ‘all’ to define a new group. It is reserved already.
Limitations in the numbers of groups and outputs
Wrong group names in fluxes and group output lines
Too many particles may cause a simulation crash.
Turn off animation output to save running time.

## Slide 11: Examples of PTM Applications
Fish-related studies (Delta smelt, Longfin smelt, Salmon): limited to larvae
  Wanger decision
  OCAP
  Temporary and permanent barriers
  DCC
  Migration studies
Sediment and Mercury

## Slide 12: Limitations
Quasi 3-D based on 1-D Model
  Many assumptions
    Rectangular channels
    Reservoirs
    Flow splits (Junctions)
Neutrally buoyant particles
  No behavior

## Slide 13: Historical Example
Based on a historical hydro tutorial
Particles are injected at Mossdale (Node 7) continuously for a day.
Outputs are in-delta particles and accumulated particle fluxes at the exports and Martinez downstream boundary.

## Slide 14
Image from USBR GIS Group
Particle
Release:
Mossdale
Flux:
Martinez
Flux: SWP & CVP
Group:
In-Delta
Flux:
Chipps
Group:
Franks

## Slide 15: Results of the Example

## Slide 16: Animation of DSM2-PTM
DSM2-PTM provides an animation tool.
  Two side-by-side panes
Use text output and animation output.

## Slide 17: Questions?

## Slide 18: Supplementary

## Slide 19: Transverse Profile

## Slide 20: Vertical Profile

## Slide 21: 3D Profile

## Slide 22: Numerical scheme
Euler Forward
  The constant velocity in one time step
Particles are bounced at the surface, bottom, and wall.
Random transverse and vertical dispersions are added.

## Slide 23: Assumption for Channels
Assume a rectangular channel based on hydrodynamic information from DSM2-Hydro, which are depth and area at each end of a channel.
  The shape of cross-sectional area is ignored.
The mid-section of a channel is linearly interpolated.

## Slide 24: Flow Split Management
DSM2 does not provide junction configurations.
When a particle hits a node, a next waterbody is determined only by the ratio of the outflows at the node.
  Does not preserve position information.

## Slide 25: Assumption for Reservoirs
A reservoir in DSM2 is represented as a completely mixed tank.
  No flow information in a reservoir.
PTM uses a similar technique to the flow split for reservoir.
  Once a particle enters into a reservoir, a next waterbody is determined randomly by the ratio of outflows and the volume of the reservoir.

## Slide 26: Real-Time Forecast
Hydro
Real-time
Flows/Stage
Forecast
Flows/Stage
PTM
Particle/Fish Information
Hydrodynamic
Information
Particle
Information

## Slide 27: 20mm Survey Locations
From DFG website